## Slide 1: LEMI’S MAIN RIG 3D DRAWING
24/10/2024
IGOR RANGEL CORRÊA FERREIRA
igorrangell@hotmail.com
(31) 99906-9584

## Slide 2: LEMI’S MAIN RIG
Fluid mixing and monitoring section
Control and operation room
Storage tanks and separators
Multiphase measurements circuit
Machine room
PIV & PLIF Equipment

## Slide 3: MAIN CHARACTERISTICS
A simplified version of LEMI’s main RIG is developed for the CFD simulations;
Only the fluid mixing section and the multiphase measurement circuit are represented in the simplified version;
The goal is to analyze the fluids behavior inside the mixer and the measurement circuit.
High Pressure Line
Low Pressure Line
HP = High Pressure (red line)
LP = Low Pressure (Orange line)

## Slide 4: INSTRUMENTATION’S POSITION
Temperature
Absolute
Pressure
Visualization window
(with high-speed cameras)
Differential pressure take 1
Gamma-ray densitometer
Differential pressure take 3
The visualization window and gamma-ray densitometer, as well as the temperature and pressure sensors are located close to the center of the multiphase measurement circuits, as follows:
Temperature
& Pressure
Visualisation Window
Dif. Pressure takes
Gamma ray
densitometer
Differential pressure take 2
End of the curve
HP = High Pressure (red line)
LP = Low Pressure (Orange line)

## Slide 5: MAIN DIMENSIONS

## Slide 6: MIXTURES OPTIONS
For setups 1, 2 & 3 :
HP = High Pressure (red line)
LP = Low Pressure (Orange line)
HP Oil (liquid)
Variable | High pressure line | Low pressure line
Max operating pressure | 15 bar(a) | 7 bar(a)
Temperature range | 20 ºC – 50 ºC | 15ºC – 50 ºC
Max gas flow rate | 463 Nm³/h | 268 m³/h
Max liquid flow rate | 60 m³/h | 60 m³/h
Liquid | Lubrax Turbina 22 | Lubrax Turbina 22 / Water
Gas | Sulphur hexafluoride | Air
Line sizes | 1", 2" | 2"
Density Ratio | 8 | >500
Horizontal line length | 30 m | 30 m
Inclinations | -90º to 90º | -90º a 90º
HP SF6 (gas)
LP Oil (liquid)
LP Air (gas)
LP Water (liquid)
*setups 1 & 2 :
Closed ends
*setup 3:

## Slide 7: MIXTURES OPTIONS
For setup 4 :
HP = High Pressure (red line)
LP = Low Pressure (Orange line)
Closed end
Variable | High pressure line | Low pressure line
Max operating pressure | 15 bar(a) | 7 bar(a)
Temperature range | 20 ºC – 50 ºC | 15ºC – 50 ºC
Max gas flow rate | 463 Nm³/h | 268 m³/h
Max liquid flow rate | 60 m³/h | 60 m³/h
Liquid | Lubrax Turbina 22 | Lubrax Turbina 22 / Water
Gas | Sulphur hexafluoride | Air
Line sizes | 1", 2" | 2"
Density Ratio | 8 | >500
Horizontal line length | 30 m | 30 m
Inclinations | -90º to 90º | -90º a 90º
HP SF6 (gas)
LP Air (gas)
Closed ends
HP Oil (liquid)
LP Water (liquid)
or
LP Oil (liquid)

## Slide 8: High pressure - Setup 1
inlet
outlet

## Slide 9: High pressure - Setup 2
inlet
outlet

## Slide 10: High pressure - Setup 3
inlet
outlet

## Slide 11: High pressure - Setup 4
inlet
outlet

## Slide 12: Low pressure – Setup 1
inlet
outlet

## Slide 13: Low pressure – Setup 2
inlet
outlet

## Slide 14: Low pressure – Setup 3
inlet
outlet

## Slide 15: Low pressure – Setup 4
inlet
outlet